## Slide 1
Date: 2025-Jan-15
Source:
Affiliations | Contact | Email
Huawei Technologies. Co. Ltd | Xu Li | lixu11@huawei.com
WI：SLB-mmW meeting # Numerology

## Slide 2: PHY Numerology (Based on 1.0 bis)
A limited set of bandwidth (choosing a set of BWs between 320 and 2560 MHz for instance)
  For example: upclock SLB by 16 times
 | 20 | 40 | 80 | 160
 | 30.72 | 61.44 | 122.88 | 245.76
NDFT | 256 | 512 | 1024 | 2048
ΔF | 120 KHz |  |  | 
TDFT | 8.333 μs |  |  | 
Ts | 32.55ns | 16.28 ns | 8.14 ns | 4.07 ns
TGI=18Ts,20M | 585.9ns | 585.9ns | 585.9ns | 585.9ns
TGI=39Ts,20M | 1269.45ns | 1269.45ns | 1269.45ns | 1269.45ns
TGI=64Ts,20M | 2083.2ns | 2083.2ns | 2083.2ns | 2083.2ns
TGI=93Ts,20M | 3027.15ns | 3027.15ns | 3027.15ns | 3027.15ns
TGI=128Ts,20M | 4166.4ns | 4166.4ns | 4166.4ns | 4166.4ns
SLB PHY numerology
mmWave PHY numerology
x16
 | 320 | 640 | 1280 | 2560
NDFT | 256 | 512 | 1024 | 2048
ΔF | 1.92 MHz |  |  | 
TDFT | 0.5208 μs |  |  | 
Ts | 2.03 ns | 1.02 ns | 0.51 ns | 0.25 ns
TGI=18Ts,320M | 36.54ns | 36.54ns | 36.54ns | 36.54ns
TGI=39Ts,320M | 79.17ns | 79.17ns | 79.17ns | 79.17ns
TGI=64Ts,320M | 129.92ns | 129.92ns | 129.92ns | 129.92ns
TGI=93Ts,320M | 188.79ns | 188.79ns | 188.79ns | 188.79ns
TGI=128Ts,320M | 259.84ns | 259.84ns | 259.84ns | 259.84ns
mmWave shares the PHY components of SLB，including Coding: Polar code, Sync sequence: FTS and STS (update), Demodulation reference signal, Phase adjustment signal, HARQ block

## Slide 3: PHY Numerology (base on 1.0 bis)
Other PHY parameters:
 | 320 M | 640 M | 1280 M | 2560 M
NDFT | 256 | 512 | 1024 | 2048
ΔF | 1.92 MHz |  |  | 
TDFT | 0.5208 μs |  |  | 
Nst | 38*4 | 76*4 | 152*4 | 304*4
Ndc | 1*4-1 | 3*4 | 3*4 | 3*4
320 MHz
320 MHz
320 MHz
320 MHz
7.68M
12.8M
10.24M
10.24M
12.8M
7.68M
7.68M
12.8M
320 MHz
320 MHz
320 MHz
320 MHz
10.24M
10.24M
12.8M
7.68M
7.68M
12.8M
10.24M
10.24M
640 M
1280 M

## Slide 4: PHY Numerology (Based on 1.0 bis)
A limited set of bandwidth (choosing a set of BWs between 160 and 2560 MHz for instance)
  For example: upclock SLB by 8 times
 | 20 | 40 | 80 | 160
 | 30.72 | 61.44 | 122.88 | 245.76
NDFT | 256 | 512 | 1024 | 2048
ΔF | 120 KHz |  |  | 
TDFT | 8.333 μs |  |  | 
Ts | 32.55ns | 16.28 ns | 8.14 ns | 4.07 ns
TGI=18Ts,20M | 585.9ns | 585.9ns | 585.9ns | 585.9ns
TGI=39Ts,20M | 1269.45ns | 1269.45ns | 1269.45ns | 1269.45ns
TGI=64Ts,20M | 2083.2ns | 2083.2ns | 2083.2ns | 2083.2ns
TGI=93Ts,20M | 3027.15ns | 3027.15ns | 3027.15ns | 3027.15ns
TGI=128Ts,20M | 4166.4ns | 4166.4ns | 4166.4ns | 4166.4ns
SLB PHY numerology
mmWave PHY numerology
x8
 | 160 | 320 | 640 | 1280 …
NDFT | 256 | 512 | 1024 | 2048
ΔF | 960 kHz |  |  | 
TDFT | 1.0416 μs |  |  | 
Ts | 4.07 ns | 2.03 ns | 1.02 ns | 0.51 ns
TGI=18Ts,320M | 73.26ns | 73.26ns | 73.26ns | 73.26ns
TGI=39Ts,320M | 77.33ns | 77.33ns | 77.33ns | 77.33ns
TGI=64Ts,320M | 260.48ns | 260.48ns | 260.48ns | 260.48ns
TGI=93Ts,320M | 378.51ns | 378.51ns | 378.51ns | 378.51ns
TGI=128Ts,320M | 520.96ns | 520.96ns | 520.96ns | 520.96ns
mmWave shares the PHY components of SLB，including Coding: Polar code, Sync sequence: FTS and STS (update), Demodulation reference signal, Phase adjustment signal, HARQ block

## Slide 5: PHY Numerology (base on 1.0 bis)
Other PHY parameters:
 | 160 | 320 | 640 | 1280 …
NDFT | 256 | 512 | 1024 | 2048
ΔF | 960 kHz |  |  | 
TDFT | 1.0416 μs |  |  | 
Nst | 38*4 | 76*4 | 152*4 | 304*4
Ndc | 1*4-1 | 3*4 | 3*4 | 3*4
160MHz
160MHz
160MHz
160MHz
3.84M
6.4M
5.12M
5.12M
6.4M
3.84M
3.84M
6.4M
160MHz
160MHz
160MHz
160MHz
5.12M
5.12M
6.4M
3.84M
3.84M
6.4M
5.12M
5.12M
320M
640 M
Maximum Bandwidth is 2560MHz

## Slide 6: Simulation results
Performance comparison among subcarrier spaces of 0.96, 1.92 and 3.84 MHz
  1.92 MHz has 0.1~1 dB lost
Parameter | Description
MCS | MCS4 (16 QAM, 3/4), MCS6 (64QAM, 3/4)
PPDU type | VHT format (11ac, 80 MHz)
Channel model | 802.11ad channel model (conference room, CR)
TX/RX | 1T1R
Fc | 73.44 GHz (Channel #8 defined in 802.11ay)
Packet size | 4096 Bytes
Other considerations | CFO, PN, and PA

## Slide 7: Super Frame
Super frame (1 ms, 8*8 radio frame)
  Super frame, half a frame, one quarter?
  Radio frame: 320Ts*12=3840Ts=15.629 μs,
  CP: 64Ts=0.260μs, OFDM: 256Ts=1.042μs, CP-OFDM: 320Ts=1.302μs
  First switching interval (GAP1): 320Ts=1.302μs, GAP2: 320Ts=1.302μs
Frame #0
Frame #1
Frame #63
……
G | G | GAP1 | T | T | T | T | T | T | T | T | GAP2
64Ts
G/T/GAP1
64Ts
G/T/GAP1
64Ts
G/T/GAP1
64Ts
G/T/GAP1
64Ts
G/T/GAP1
64Ts
G/T/GAP1
64Ts
G/T/GAP1
64Ts
G/T/GAP1
64Ts
G/T/GAP1
64Ts
G/T/GAP1
64Ts
G/T/GAP1
64Ts
G/T/GAP2
Example:

## Slide 8: Radio Frame Structures
G | G | G | G | G | G | G | G | G | GAP1 | T | GAP2
15.629μs with symbol # equal to 12
G | G | GAP1 | T | T | T | T | T | T | T | T | GAP2
G | G | G | G | G | G | G | G | G | G | G | G
T | T | T | T | T | T | T | T | T | T | T | T
G | G | GAP1 | T | T | GAP1 | G | G | GAP1 | T | T | GAP2
①
②
③
④
⑤
Symbol # | CP | CP-OFDM (GAP1) | GAP2
14 | 18Ts，73.26ns | 274Ts，1.115μs | 278Ts，1.131μs
13 | 39Ts，158.37ns | 295Ts，1.201μs | 300Ts，1.221μs
12 | 64Ts，260.48ns | 320Ts，1.302μs | 320Ts，1.302μs
11 | 93Ts，378.51ns | 349Ts，1.420μs | 350Ts，1.425μs
10 | 128Ts，520.96ns | 384Ts，1.563μs | 384Ts，1.563μs
For 802.11ad/ay device:
short beamforming interframe space (SBIFS)
aSBIFSTime=1us
aSBIFSAccuracy=[0, +0.03] us
LBIFS=6*aSIFStime=18 us
MBIFS=3*aSIFStime=9 us
MBIFS shall be used between the BTI and the A-BFT and between the ISS, RSS, SSW Feedback, and SSW ACK.
LBIFS shall be used between transmissions employing different DMG antennas and when the recipient STA is expected to switch DMG antennas

## Slide 9: Q&A