## Slide 1: WI: SLB-mmW Meeting # Spatial Streams & MCS
Date: 2025-Jan-15
Source:
Affiliation | Contact | Email
Huawei Technologies. Co. Ltd | Xiuzhu Yang | yangxiuzhu@huawei.com
Huawei Technologies. Co. Ltd | Xu Li | lixu11@huawei.com

## Slide 2: Contents
Spatial Streams
MCS
Discussions
Next Steps

## Slide 3: Spatial Streams

## Slide 4: Spatial Streams
Spatial streams: several streams transmitted on multiple spatial dimensions by using multiple antennas at communications link.
Transmit chains: several chains for transmitting signals.

## Slide 5: Spatial Streams - Structure 1
Spatial Stream Parser
…
Spatial Stream Parser divides the output of the modulation mapper into several groups of bits. These sequences of the bits are different spatial streams.
different spatial streams
Modulation mapper
Precoding
Resource element mapper
OFDM signal generation
antenna port 1
Resource element mapper
OFDM signal generation
antenna port 2
Resource element mapper
OFDM signal generation
antenna port x
…
Scrambling
Encoder
codeword
After precoding, different spatial streams are mapped to different transmit chains.
different transmit chains

## Slide 6
Scrambling
Encoder
Spatial Stream Parser
…
different spatial streams
codeword
Modulation mapper
Precoding
Resource element mapper
OFDM signal generation
antenna port 1
Resource element mapper
OFDM signal generation
antenna port 2
Resource element mapper
OFDM signal generation
antenna port x
…
different transmit chains
Modulation mapper
Modulation mapper
Spatial Stream Parser divides the output of the scrambling into several groups of bits. These sequences of the bits are different spatial streams.
After precoding, different spatial streams are mapped to different transmit chains.
Spatial Streams - Structure 2

## Slide 7: MCS

## Slide 8: MCS (Modulation and Coding Scheme)
MCS is a scheme that determines the modulation and coding.
  Common modulations include BPSK, QPSK, 16-QAM, etc.
  Common codes include Polar code, etc.
  Considering the SNR imbalance over spatial streams, MCSs or modulations over different spatial streams could be different.
  Equal Modulation
  Unequal Modulation
  Equal MCS
  Unequal MCS

## Slide 9: Suggested MCS Table
MCS index | Modulation | Number of Bits Per Symbol | Code rate
1 | BPSK | 1 | 
2 | BPSK | 1 | 
3 | BPSK | 1 | 
4 | BPSK | 1 | 
5 | BPSK | 1 | 
6 | QPSK | 2 | 
7 | QPSK | 2 | 
8 | QPSK | 2 | 
9 | QPSK | 2 | 
10 | QPSK | 2 | 
11 | 16-QAM | 4 | 
12 | 16-QAM | 4 | 
13 | 16-QAM | 4 | 
14 | 16-QAM | 4 | 
15 | 16-QAM | 4 | 
16 | 64-QAM | 6 | 
17 | 64-QAM | 6 | 
18 | 64-QAM | 6 | 
19 | 64-QAM | 6 | 
20 | 64-QAM | 6 | 
The suggested MCS table includes four modulation types, namely, BPSK, QPSK, 16-QAM, 64-QAM modulations.
64-QAM modulation needs to be supported.
Higher-order modulations and different code rates need to be discussed.

## Slide 10: Discussions
The transmitter block architecture of SparkLink mmWave.
Should we support 256-QAM modulation or higher-order modulation?
Should we support unequal modulation or unequal MCS over different spatial streams?

## Slide 11: Next Steps
Continue the study of spatial streams & MCS
Adapt the spatial streams & MCS to SparkLink mmWave architecture and framework

## Slide 12: Thank you