## Slide 1: SI: SLB-mmW Meeting # Multi-Carrier Operation Preliminary Concept
Date: 2025-03-06
Affiliation | Contact | Email
Huawei Technologies. Co. Ltd | Dor Chay | dor.chay@huawei.com
Source:

For approval
For discussion
For information




## Slide 2: Contents
Motivation
Advantages of Multi-Carrier Operation
Challenges of Multi-Carrier Operation
Preliminary Concept
Next Steps

## Slide 3: Motivation
Multi-Carrier Operation (MCO, aka Multi-Link Operation or Carrier Aggregation) refers to a technique used in wireless networks to combine multiple frequency bands (carriers) to increase the overall data transfer rate, capacity, and reliability of the network
In the context of Sparklink, we would like to have an inter-band non-contiguous MCO capability between FB1 (sub-7GHz) and FB2 (mmWave)
…
…
Frequency
FB1 (sub-7GHz)
FB2 (mmWave)
Carrier 1
Carrier 2

## Slide 4: Advantages of Multi-Carrier Operation
Increased Throughput: By aggregating multiple carriers, each node can transmit more data in the same amount of time, which results in higher data rates. This is especially useful for high-bandwidth applications like streaming, gaming, and large file transfers.
Reduced Latency: MCO can help reduce latency by splitting the data traffic across multiple links. For example, if one link has high traffic or congestion, another link can be used to send data, improving the response time of the network.
Improved Reliability: By transmitting data over multiple links, MLO can avoid disruptions caused by interference or signal degradation on a single link. If one band becomes crowded or experiences poor conditions, another band can handle the traffic, leading to a more stable connection. This is extremely important in mmWave.

## Slide 5: Advantages of Multi-Carrier Operation
Better Coverage: Multi-carrier aggregation can help provide more reliable coverage in areas with high demand for bandwidth.
Improved Spectrum Efficiency: Multi-carrier operation allows the G-node to schedule available spectrum more effectively, enabling better utilization of different frequency bands.

## Slide 6: Challenges of Multi-Carrier Operation
Complexity: Managing multiple links simultaneously requires complex coordination and algorithms. The device must decide how to distribute traffic between the different links to avoid interference and congestion while ensuring optimal performance.
Power Consumption: Aggregating multiple carriers might increase power consumption on both the G-node and the T-nodes. This could be a concern for battery-powered devices like smartphones or laptops.

## Slide 7: Preliminary Concept
Architecture – a single upper MAC layer over Multiple lower MAC & PHY layers
FB1 Channel
FB2 Channel
Application Layer
Transport & Network Layers
Link Control Layer
Upper MAC Layer
Data Link Layer
Access Layer
FB1 PHY Layer
FB2 PHY Layer
G-node
FB1 Lower MAC
FB2 Lower MAC
Application Layer
Transport & Network Layers
Link Control Layer
Upper MAC Layer
Data Link Layer
Access Layer
FB1 PHY Layer
FB2 PHY Layer
T-node
FB1 Lower MAC
FB2 Lower MAC

## Slide 8: Preliminary Concept
Minimum Effective Bandwidth
  SLB 1.0 bis @ 5GHz: 20MHz
  SLB-mmW @ 60GHz: 160MHz (larger BW of 320MHz is considered)
  MCO total: 180MHz
Maximum Effective Bandwidth
  SLB 1.0 bis @ 5GHz: 160MHz (may be more in 6GHz + )
  SLB-mmW @ 60GHz: 1280MH z (larger BW of 2560MHz is considered)
  MCO total: 1440MHz
Primary & Secondary Carriers
  The Primary Carrier (PC) is the anchor carrier used for association, control, power management, data transmission & reception
  The Secondary Carrier (SC) is the supporting carrier used mainly for data transmission & reception
  In Sparklink, the primary carrier should be the FB1 carrier. This is aligned with the study work and assumptions done so far for FB2 beam management and association

## Slide 9: Preliminary Concept
Logical State Machine
  The state machine assumes the PC is always active and available
  The changes in state is a result of changes to the SC
  When in “SC Unconfigured” state we work in single carrier over the PC
  When in “SC Configured” state we can activate carrier aggregation
  “SC Deactivated” & “SC Activated” sub-states are for power management
SC Unconfigured
SC Configured
SC Deactivated
SC Activated
SC Configuration
SC Removal
Activation
Deactivation

## Slide 10: Preliminary Concept
SC Configuration / Removal
  Configuration & removal are subject to the SC link quality (e.g. RSRP, PER etc.)
  E.g. beam management failure will cause removal of SC
Power Management (SC Activation / Deactivation)
  The primary carrier is typically in an “always-on” state
  The secondary carrier is dynamically activated/de-activated
  Activation/Deactivation is controlled by the G-node using MAC Control Element (CE)
  Activate SC when:
    Buffer size > BufferSizeActThreshold (Threshold can be adjusted to PC data rate) or
    Head of queue delay > HoqDelayActThreshold
  Deactivate SC when:
    Buffer size < BufferSizeDeactThreshold (Threshold can be adjusted to PC data rate) or
    Head of queue delay < HoqDelayDeactThreshold
  Need consider the option of activate/deactivate separately for UL/DL

## Slide 11: Preliminary Concept
Measurement Items Required from T-node for Activation Decision:
  RSRP [dBm]
  RSSI [dBm]
  SNR [dB]
  PER [%]
  Buffer Status [KB]
  Head of Queue Delay [usec]
  Tx Power Headroom [dBm]

## Slide 12: Preliminary Concept
FB2 Channel
Traffic Stream to Carrier Mapping & Load Balancing
  Traffic streams to carrier mapping is controlled by the G-node
  T-node can send a traffic stream to carrier mapping request, indicating its preference
  This mapping can be used for load balancing
  E.g. when user has an ongoing video call and file transfer, they can be split to ensure the quality of the call is not affected by the file transfer
Video call
File Transfer
G-node
Video call
File Transfer
T-node
FB1 Channel
Without MCO
Video call
File Transfer
G-node
Video call
File Transfer
T-node
FB1 Channel
With MCO

## Slide 13: Preliminary Concept
Global Frame Number
  The frames at the receiver side should be ordered according to the Global Frame Number (GFN)
Unique Identifier
  The node unique identifier across the multiple carriers remains the MAC Address

## Slide 14: Thank you