## Slide 1: WI：SLB-mmW meeting 1 Latency and Reliability for SparkLink over mmWave Bands: A Physical Layer Perspective
Date: 2024-11-19
Source:
Affiliation | Contact | Email
University of Thessaly Greece | Prof. Theodoros Tsiftsis | tsiftsis@uth.gr

## Slide 2: Outline
SLB Specs and Applications
Physical Layer Latency
  SLB Specs
  Latency (definition, SLB latency)
  Reliability (definition, SLB reliability)
mmWave Impact on Latency & Reliability
SLB’s Rivalries & SLB Competitive Adv
mmWave for V2X Applications
  Technical Challenges
  Use Cases
My Contributions to SLB Project

## Slide 3: SLB Specs
Parameters | Specification value
Working bandwidth | 20/40/60/80/100/160/320MHz
Multi-access mode | OFDMA
Duplex mode | TDD
Radio frame configuration | Normal CP: 14 Extended CP: 12
Number of spatial multiplexed data streams | G node is in support of the transmission of maximum 8 streams. T node is in support of the transmission of maximum 4 streams.
Modulation scheme | QPSK/16QAM/64QAM/256QAM/1024QAM
Channel coding | Polar/RS
Length of physical frame | 20.833μs
Retransmission mode | HARQ at the physical layer, ARQ at the link layer

## Slide 4: SLB Applications
Smart cars
Intelligent manufacturing
Smart terminals
Smart homes

## Slide 5: Latency Definition
End-to-End
over-the-air transmission delay
User Plane (data link layer)
the one-way time it takes to successfully deliver an application layer packet/message from the radio protocol layer entry point to the radio protocol layer exit point via the radio interface in both UL/ DL directions
Control Plane (network layer)
the transition time from a most “battery efficient” state (e.g., idle state) to the start of continuous data transfer (e.g., active state)
queuing delay
processing/computing delay and retransmissions

## Slide 6: Physical Layer Latency
Physical layer latency can be divided into the following five components:
  is the time-to-transmit latency, which corresponds to the time to transmit a packet
  is the signal propagation time from the transmitter to the receiver
  is the time to perform the encoding and decoding, and also the channel estimation in the initial transmission
  is the time taken by retransmission
  is the pre-processing time for the signaling exchange such as connection request, scheduling grant, channel training and feedback, and queuing delay

## Slide 7: SLB Latency
Ultra-Low Latency (Air Interface) < 20.833μs
  CP-OFDM waveform
  Ultra-short frame structure and a flexible scheduling scheme of time domain resources

## Slide 8: SLB Latency
Ultra-short frame structure
  Overhead constrain frame length
  Even worse in TDD scheme adopted by SBL
  Frame structure length: 20.833μs
  SLB designs a frame structure with 48 frames in one superframe equal to 1ms
Radio Frame #01
Radio Frame #02
Radio Frame #46
Radio Frame #47

## Slide 9: SLB Latency
Flexible scheduling scheme of time-domain resource
  Scheduling scheme of time-domain resources that corresponds to different sizes of packets.
  Minimum scheduling units for small packets (1 frame, 20.833 ms) and large packets (6 frames, 125 ms)
  The transmission period of large packets is a multiple of the minimum scheduling units, which can be equal to 6, 12, ., 48 frames.
Radio Frame #01
Radio Frame #02
Radio Frame #46
Radio Frame #47

## Slide 10: Reliability
  Reliability: Probability that a data of size 𝐷 is successfully transferred with a time period 𝑇 (Aim: )
  Reliability per Node: The transmission error probability, queuing delay violation probability and proactive packet dropping probability
  Control channel reliability: The probability of successfully decoding the scheduling grant or other metadata
No packet drop
No packet delay
No erroneously decoding

## Slide 11: SLB Reliability
Coding Scheme
  Polar code to correct errors
    capability for large code lengths
    superb performance when correcting random errors
  SLB adopts cyclic redundancy check (CRC)-assisted Polar codes with successive-cancellation list (SCL) decoders

## Slide 12: Reliability SLB vs WiFi 6 [1]

## Slide 13: SLB Reliability
Retransmission
  HARQ is deployed to improve the reliability while decreasing the number of retransmissions.
    time variability of channels
    multipath effect
    other unpredictable interferences

## Slide 14: Coupling Latency & Reliability
Under the constraints of a URLLC service, the definition of reliability should be coupled to the latency requirement
When latency requirement is absent (theoretically infinite) then transmitting at a rate that is lower than channel capacity offers perfect reliability
Definition for Reliability (application perspective): The probability that the latency does not exceed latency constraint (deadline)
Outage as the probability that it does

## Slide 15: mmWave Impact on Latency & Reliability
Pros
High Bandwidth
  higher data rates
High Capacity
  more simultaneous connections to support dense deployments
Low Latency (Potential)
  due to less signal dispersion

## Slide 16: mmWave Impact on Latency & Reliability
Cons
High Path Loss and Penetration Loss
  higher path loss and are severely attenuated by obstacles
  impacts reliability.
Susceptibility to Blockage
  Even minor obstructions can significantly impact signal strength, potentially leading to connection drops and impacting reliability
Increased Complexity
  advanced beamforming techniques to overcome the inherent limitations of the frequency band
Rain Fade

## Slide 17: SLB’s Rivalries & SLB Competitive Adv
WiFi –Only IEEE 802.11bd –MG V2X will support 60GHz band
Bluetooth
ZigBee
Latency & Reliability

## Slide 18: SLB’s vs WiFi 6 (IEEE 802.11ax)

## Slide 19: SLB’s vs WiFi 7 (IEEE 802.11be)

## Slide 20: SLB’s vs (IEEE 802.11p & 802.11bd)
Latency for IEEE802.11p is 50ms
No latency is referred for IEEE802.11bd

## Slide 21: Technical Challenges in mmWave
Limited research and measurements results.
Channel sounding is the use of directional beams which require fast beam switching under high mobility.
For the design of mmWave V2X radio access, it is necessary to characterize the mmWave radio propagation in V2X scenarios
Path loss
Shadowing
Blockage
Fast fading

## Slide 22: mmWave for V2X Applications
ITU-R provided a guideline on the use of 57-66 GHz band for intelligent transport system (ITS) applications.
In Europe 63-64 GHz band is currently designated by CEPT/ECC.

## Slide 23: Key Challenges for SLB on mmWave-Based V2X Applications
Initial Beam Alignment
Beam Tracking to maintain the mmWave link
Beam Recovery
Beam Management

## Slide 24: Use Cases for SLB on mmWave-Based V2X Applications
Cooperative perception
High definition (HD) 3D map download
Sensor data upload
High-speed mobile broadband Internet access
Data rate: 10s to 100s of Mbps per application and so if we were to support multiple applications simultaneously, up to Gbps data rate is likely required.
Latency: 10 ms -100 ms is required for safety applications such as cooperative perception

## Slide 25: My Contribution to the SparkLink over mmWave Bands Project (1)
Beam Alignment Latency: Time duration required for the completion of the beam alignment procedure
  Beam alignment latency refers to the duration required to finalize the beam alignment procedure in V2X communication, commencing with the onset of a beam alignment request. This latency includes multiple stages, such as transmitting the request, obtaining the response, calculating beam angles, and modifying antenna directions.
  Simulations will be conducted for:
    Various number of antennas,
    Path Loss, Fading, LoS/NLoS etc.

## Slide 26: My Contribution to the SparkLink over mmWave Bands Project (2)
Alignment Probability: This metric serves as a crucial indicator of the system's reliability, reflecting the probability of the beam correctly matching with the receiver's beam within a defined tolerance.
  Simulations will be conducted for:
  Beam sweeping
  Angle of arrival (AoA)/angle of direction (AoD) estimation
  Side information beam alignment methods

## Slide 27: My Contribution to the SparkLink over mmWave Bands Project (3)
Effective Achievable Rate: A fundamental parameter assessing the efficacy of data exchange following the alignment procedure.
Simulations will be conducted for:
  Modulation techniques
  Beamforming design,
  Transmission diversity

## Slide 28: References
[1] Gao M, Wan L, Shen R, Gao Y, Wang J, Li Y, Vucetic B. SparkLink: A short-range wireless communication protocol with ultra-low latency and ultra-high reliability. Innovation (Camb). 2023 Jan 31;4(2):100386.
[2] J. Tan et al., "Beam Alignment in mmWave V2X Communications: A Survey," in IEEE Communications Surveys & Tutorials, vol. 26, no. 3, pp. 1676-1709, thirdquarter 2024.
[3] T. Shimizu, V. Va, G. Bansal and R. W. Heath, "Millimeter Wave V2X Communications: Use Cases and Design Considerations of Beam Management," 2018 Asia-Pacific Microwave Conference (APMC), Kyoto, Japan, 2018, pp. 183-185
[4] CEPT/ECC, Harmonised use of the 63.72-65.88 GHz frequency band for Intelligent Transport Systems (ITS) https://docdb.cept.org/download/1563
[5] M. Giordani, A. Zanella, T. Higuchi, O. Altintas and M. Zorzi, "On the Feasibility of Integrating mmWave and IEEE 802.11p for V2V Communications," 2018 IEEE 88th Vehicular Technology Conference (VTC-Fall), Chicago, IL, USA, 2018, pp. 1-7
[6] R. I. Abd and K. S. Kim, "Protocol Solutions for IEEE 802.11bd by Enhancing IEEE 802.11ad to Address Common Technical Challenges Associated With mmWave-Based V2X," in IEEE Access, vol. 10, pp. 100646-100664, 2022

## Slide 29: References
[7] Y. Cao, X. He, C. Yu and C. Yin, "Reliability and Latency of MmWave Communications Based on Blockage Avoidance in Internet of Vehicles," 2021 13th International Conference on Wireless Communications and Signal Processing (WCSP), Changsha, China, 2021, pp. 1-5
[8] CAR 2 CAR Communication Consortium. “Next Generation V2X –IEEE 802.11bd as fully backward compatible evolution of IEEE 802.11p,” February 2023. [https://www.car-2-car.org/documents/general-documents ]
[9] P. Popovski et al., "Wireless Access in Ultra-Reliable Low-Latency Communication (URLLC)," in IEEE Transactions on Communications, vol. 67, no. 8, pp. 5783-5801, Aug. 2019